## Slide 1: CECOM - EOA Metadata Assumptions and Decisions
CBM+ File and Messaging Workshop
June 12-14, 2012
Pam Ludwig
Dr. Xinxin Wang
CECOM CBM+
wang_xinxin@bah.com

## Slide 2: Site
What platform types will be considered to have a site?
  End-item - platforms (e.g. a TQG or CPP)
  Reusable and replaceable units – RU (e.g. an engine)
  Each asset model has a prototype site (of LOGSA or Army Enterprise)
  LOGSA Site + Base 16 of NIIN
  Each asset instance has an unique instance site (of CECOM)
  CECOM site + unique number
What will be used as templates?
  Prototype component tree and measurement configuration for a model of assets
Will ABCD Sites be templates or individual platforms?
  Instance site (individual platform)
Will an ABCD file contain more than one site?
  LVL04.SENS segment site = LVL00.PLAT segment site (end-item site)
  LVL04.SENS asset site may be different from the LVL00.PLAT segment site
What information/identifiers will be associated with a site and how?
  NIIN or CAGE/PartNo (will be assigned a surrogate NIIN)
  NIIN (real or surrogate) is site_id; NIIN and/or CAGE/PartNO will be in user_tag_ident

## Slide 3: Segment
Where do you obtain your Bill of Materials (BoM) and how do you translate it into the concept of segments?
  We have no login account to LMP and only have a copy of TQG 805B’s BoMs. We currently use IETMs. But we had some studies on BoM.
  Model Prototype Component Tree – Derived from IETMs; candidate components in the tree include:
    A monitored component (RU, assembly, or part)
    An RU or assembly that contains a candidate component
  Each component in the tree will have a segment entry in the model prototype site
To what level of granularity will segments be specified?
  To a component that is monitored (associated with a measurement location)
What segment will be used at the global level in ABCD?
  Top segment for a platform or serialized RU
What information will be associated with a segment and how?
  Site – prototype site for a prototype segment; or instance site for an instance segment
  ID - Top segment of a prototype or instance tree: 0
  Other segments: assigned a unique ID within the site – increased by 1
  Name
  Type – Used the segment types defined in the Army type DB:
  platform - ‘Platform’; RU - ‘SRU’, Assembly – ‘Assembly’, Others – ‘Component’
  NIIN and/or CAGE/PartNo(?) of each component, if any, will be stored in the user_tag_ident
  The composition of Name, NIIN, CAGE/PartNo must be unique under an assembly
  SMR code and/or CAGE/PartNo will be stored in the segment_chr_data table

## Slide 4: Asset
Will assets be tracked?
  All assets are added to the CECOM asset site with unique ID
  Each asset has an ‘as-built’ instance segment tree in an instance site, which is cloned from its model prototype segment tree
If Assets will be tracked:
  How will Assets be tracked on Segments?
    Entries in the asset_on_segment table
    Each installed asset can be associated with one or multiple segments of its ascendant assets
  What information will be associated with an asset and how?
    Site – CECOM asset site
    ID – unique among all CECOM assets
    Type – An asset type of NIIN in a LOGSA type DB
    SN, VIN, Other unique asset ID(?) for asset is stored in serial_number field
    SN/VIN/OtherAssetID, NIIN and/or CAGE/PartNo(?) will be stored in the user_tag_ident
    Other info (e.g. Bumper Number, Owning Unit and Region, etc.) will be stored in the asset_chr_data table
    Model key
    Top segment key of the instance segment tree

## Slide 5: Measurement Location (Sensor)
How will identical meas_locations be tracked across sites?
  A cloned segment measurement location has same name and type from the original prototype measurement locations, and their monitored segments define a relationship in the segment_child table (see next item)
  An entry in the segment_child table links a cloned segment tied to a cloned measurement location to the corresponding original segment tied to an original measurement location
How will meas_locations be tied to segments or assets?
  Monitored segments are stored in the segment_* fields for all measurement locations
  Monitored assets are stored in the asset_* fields for instance asset meas. Locations only
  Measurement Location Site and Id=0 is the top segment of the component tree
What information will be associated with a meas_location and how?
  Site – prototype site for a prototype location, instance site for an instance location
  Name – combination of name and segment_* is unique in the site
  Type – ‘Data Set Group’ and ‘DA’, ‘DM’, ‘SD’, ‘HA’, ‘PA’ and ‘AG’
  segment_or_asset indicator
  Monitored segment (and asset for asset measurement locations only)
  Data source type
  Engineering unit, update interval, collection duration
  Alarm region info

## Slide 6: Measurement Location (Data Event Set)
Will data event sets be tracked?
  Yes – each data event set has a measurement location in meas_location table
If so, what will be the process to track configuration changes?
  Using meas_loc_assoc table – an entry associates a data event set measurement location to a CBM layer measurement location

## Slide 7: Other
What will be the scope of a file, in terms of:
  Time frame covered by file
    Will follow ABCD File Time Series Best Practices
    Long session will be broken into multiple sequences
  Any fragmentation of data sets into multiple files
    Not for EOA II, but may do it after EOA II to break up a large file by grouping a subset of zVariables associated with an serialized asset
What zVariable naming convention will you use?
  We currently follow the best practices and have not added any new tags lower than LVL90
Which best practices will be leveraged?
  ABCD File Best Practices
  LOGSA File Naming Conventions
What LVL90+ metadata will be used?
  Probably, but we have not made any decision yet. Impact and AMSAA add different LVL90 tags