## Slide 1: Repeatable Registration Processes
Populating Data to MIMOSA Registry
CBM+ File and Message Workshop
June 12-14, 2012
Dr. Xinxin Wang
Supporting CECOM SEC
wang_xinxin@bah.com

## Slide 2: Objectives and Assumptions
Objectives
  Leverage previous registration work done by TACOM and LOGSA as much as possible
  Resolve issues found during CECOM’s work on populating data to MIMOSA registry
  Define criteria used to determine which objects to add to the CBM+ registry
  Define repeatable registration processes that can be applied to all CECOM scenarios
Assumptions
  Focus on the hard assets (e.g. platforms and equipment) of the Army
  Focus on adding/updating CBM objects

## Slide 3: Used Terms
Asset – An item that has value to be tracked for CBM (e.g. platform, valuable Replaceable Unit or sensor)
Platform – A system (end item) of which the health condition needs to be monitored and assessed as a whole
Replaceable Unit (RU) – A stock item that can be installed on one or multiple platforms and replaced with another RU of the same model
Model – A class of asset that has the same component tree structure
Assembly - A component in a model component tree that is not an RU and has subcomponents
Part – A subcomponent in a model component tree that is not an RU and has no subcomponent
Source Maintenance and Recoverability (SMR) Code – A 5-letter code assigned to each component in an Interactive Electronic Technical Manual (IETM): first 2 letters are source code, 3rd and 4th letters are maintenance code and the 5th letter is the recoverability code

## Slide 4: Used Terms (continued)
Segment – A MIMOSA object that represents a component in a component tree of an asset or a model. A segment for an asset is called an Instance Segment and a segment for a model is called a Prototype Segment.
Measurement Location – A MIMOSA object that represents a CBM measurement (e.g. sensor signal or status assessment) for an asset or a model. A measurement location for an asset is called an Instance Measurement Location and a measurement location for a model is called a Prototype Measurement Location.
Site – A container that groups MIMOSA objects (e.g. segments and measurement locations) for an asset or a model. A site for an asset is called an instance site and a site for a model is called a prototype site.

## Slide 5: Registration Processes
Model Registration Process
  Add/Update models and their associated prototype component trees for platforms and RUs
Measurement Configuration Process
  Add/Update prototype measurement locations for a model or instance measurement locations for an asset*
Asset Registration Process
  Add/Update platforms, valuable RUs or other serialized items
Replaceable Unit Installation Process
  Install RU assets on target segments of parent assets
*The process currently doesn’t handle custom instance measurement configuration for an asset. If we need to support custom measurement locations for each individual platform or even RU, the process will be updated to handle Instance measurement Configuration as well.

## Slide 6: Model Registration Criteria
Model – Identified by NIIN or CAGE/PartNo and for:
  Platform: Determined by MACOM
  RU asset (stock and replaceable item) - SMR source code is: PA, PB, PC, PG or PH
Model Prototype Component Tree* – Derived from Interactive Electronic Technical Manuals (or Bill of Materials?); candidate components in the tree are:
    A monitored component (RU, assembly, or part)
    An RU or assembly that contains a candidate component
  Each component in the tree:
    Includes Name (mandatory), SMR code, NIIN, CAGE/PartNo
    Has a Unique Composite Key for each component under an assembly: Name, NIIN, CAGE/PartNo
Site – Each model has a site for its prototype components
*Another option is to derive a model component tree from a Bill of Materials (MBOM, PBOM or RBOM?) with the assumption that BOMs already exist in relational form in the LMP (Logistics Modernization Program). There is an indicator of stock item and an indicator of recursive item (repairable item?) for each component in a BOM.

## Slide 7: SMR Code

## Slide 8: Hypothetical Models
Site M3
Site M2
Site M1
M1
M1:A1
M1:R2
M1:R1
M2
M2:R3
M2:P1
M3
M1:R1R3
M1:R1P1
M1:R2R3
M1:R2P1
M
Top component of the prototype tree of Model ‘M’
M:A
An assembly ‘A’ in the prototype tree of model ‘M’
M:R
An RU ‘R’ in the prototype tree of model ‘M’
M:P
A part ‘P’ in the prototype tree of model ‘M’
Component relationship
Clone of a component relationship
Inheritance relationship
Clone of a component from an inherited model
Note: Cloned subcomponents may not be needed if we make some assumptions for sensor configuration. Adding these components makes sensor configuration more flexible (more discussions later).

## Slide 9: Models in Registry
Models added for platforms or valuable RUs only
Each model has a prototype site in site table
  If a model doesn’t have a NIIN, but has CAGE/PartNo, a unique surrogate NIIN will be assigned to the model (start at 1000000000 and increase by 1)
  Site code = LOGSA site(?)* + base 16 NIIN (real or surrogate)
  Site id = NIIN (real or surrogate)
  Site type = ‘Platform’ for platforms or ‘Component’ for RUs
  User tag identification = real NIIN and/or CAGE/PartNo
Each model has an entry in model table
  Added to a LOGSA(?)* database for NIINs
  Model Id = NIIN (real or surrogate)
  Segment_* = top segment of the prototype tree
  Asset type = asset type of NIIN in asset_type table
*Should we use a site of Army Enterprise?

## Slide 10: Model Component Tree in Registry
Each model has a prototype component tree represented by the following MIMOSA tables:
  segment table: each non-cloned component and a top cloned component has an entry (cloned subcomponent of an RU model TBD)
    Segment site = Prototype site for the model
    Segment Id = NIIN for the top component; 1000000000 (real NIIN) or 0 (surrogate NIIN) for first subcomponent; max(ID>=1000000000)+1(real NIIN) or max(ID<1000000000)+1( surrogate NIIN) for next added subcomponent*
    Segment type = ‘Tactical Wheel Vehicle (TWV) System’ or ‘Ground Platform’ for platform; ‘SRU’ for RUs; ‘Assembly’ for assemblies and ‘Component’ for parts. (These types are defined in a database of the Army enterprise.)
    User Tag Identification = NIIN (real or surrogate)
    Each segment may be associated with an entry in segment_chr_data table to store other keys and additional info (e.g. CAGE/PartNo)
  sg_network_connect table: each parent-child component relationship has an entry using the ‘Component Structure Network’
  segment_child table: each inheritance (clone) relationship has an entry
* MIMOSA ‘s segment Id can only have 10 digits

## Slide 11: Model Registration Process
Add a new model and its associated prototype component tree for a class of platforms or RUs as well as synchronize its previously added assets with the model
Add new prototype components for an existing model and synchronize the cloned instance component trees for existing assets of the model as well as the cloned prototype component trees of ascendant models with the component trees of the updated model
Input:
Mandatory: Model
  Mandatory: NIIN or CAGE/PartNo
  Conditional: Name (for new model)
  Conditional: SMR Code (for RU)
Mandatory :Type
  Platform: ‘Ground Platform‘ or ‘Tactical Wheel Vehicle System‘
  RU: ‘SRU’
Optional: Other info (e.g. manufacturer)
Optional: Component tree, each component in the tree has:
  Mandatory: Name,
  Optional:
  SMR code,
  NIIN or CAGE/PartNo
Output:
A site for the model prototype segments exists in the site table
A asset type for the model exists in the asset_type table
New or updated model entries exist in the model table for the model and the models of valuable sub-RUs
New or updated prototype segments exist in the segment table for the model and the models of valuable sub-RUs
Entries in the se_network_connect table exist to define the component relationships in the prototype segments
Entries in the segment_child table exist to define component inheritance relationships in the prototype segments
The cloned prototype segment subtrees in all existing ascendant models are in sync with the model
The cloned instance segment tree for all existing assets of the model are in sync with the model
The assets of a new model previously added are in sync with the model
Model Registration Process

## Slide 12: Measurement Configuration Criteria
Measurement Location – for segment or asset
  Segment measurement location: monitors a functional item, e. g. consumable items such as fuel consumption
  Asset measurement location: monitors a physical item of an asset (e.g. usage stress) and will always be associated with the asset independent of the platform on which the asset is installed
Prototype Measurement Configuration – for a model
  A model inherits (clone) only the segment measurement locations from its descendant models
  A model can have more segment or asset measurement locations
Instance Measurement Configuration – for an asset
  An asset inherits (clone) all measurement locations from its model
  Each platform can have additional custom measurement locations? - not considered currently
Alarm Information – for original measurement location
  Each non-cloned measurement location has associated alarm information
  Each cloned measurement location uses the same alarm information of its original location
Associations Between Measurement Locations – not considered currently
Measurement Location Site
  Use model site for prototype measurement locations of a model
  Use asset site for instance measurement locations of an asset

## Slide 13: Hypothetical Prototype Measurement Configuration
Site M3
Site M2
Site M1
M1
M1:A1
M1:R2
M1:R1
M2
M2:R3
M2:P1
M3
M1:R1R3
M1:R1P1
M1:R2R3
M1:R2P1
Notes:
The measurement locations that monitor a functional item - segment (in pink) are cloned to ascendant models; the measurement locations that monitor an asset (in yellow) are not cloned to ascendant models.
The alarm entries for each cloned measurement location are cloned to ascendant models for easy look up.
Do we have the need to define measurements mounted on a cloned subcomponent (e.g. M1:A3)? If we don’t, there is no need to add cloned subcomponents of an inherited model to a prototype tree.
We do not currently consider the associations between measurement locations.
Measurement ‘S’ that monitors a function item (segment) of model ‘M’ and mounted on component ‘C’
Measurement ‘A’ that monitors an asset of model ‘M’ and mounted on component ‘C’
M1:A3
M2:A2
M3:A1
M:A
M1:R3
M2:F2
M3:F1
M:F
C
C
Measurement ‘S’ of model ‘M’ cloned from a measurement of an inherited model
M:S
C
M1:R2F1
M1:R1F1
M2:F1
M1:R2F2
M1:R1F2
Alarm entry linked to a measurement location
Cloned alarm entry linked to a measurement location

## Slide 14: Prototype Measurement Configuration in Registry
Each measurement location (includes locations for a data event group) has an entry in meas_location table associated with the model site
Each measurement location of CBM layer types has an entry in num_alarm_reg table for alarm information

## Slide 15: Prototype Measurement Configuration Process
Add/update prototype measurement locations of a model
Synchronize the instance measurement locations for all existing assets of the model with the updated prototype measurement locations
Synchronize the cloned measurement configuration for all ascendant models with the measurement configuration of the model
Input:
Mandatory: Model NIIN
Mandatory: List of measurement locations, each of the locations includes:
  Mandatory: name, type(Data event group, DA, DM, SD, HA, PA, AG)
  Mandatory: segment or asset indicator, monitored segment
  Conditional: engineering unit (for CBM layers), update interval (for DA)
  Conditional (for CBM layers): alarm info (e.g. alarm type, min, max, typical, effective data, etc.)
  Optional: data source type
Output:
New or updated prototype measurement locations exist in the meas_location table for the model
New or updated alarm entries exist for each measurement locations of CBM layer in the num_alarm_reg table
The cloned measurement locations for all existing ascendant models are in sync with the measurement locations of the model
The instance measurement locations for all existing assets of the model are in sync with the measurement locations of the model
Prototype Measurement Configuration Process

## Slide 16: Asset Registration Criteria
Asset – Identified by NIIN and asset ID: SN/VIN/Other IDs(?):
  Platforms: Determined by MACOM
  Valuable RUs:
    Stock and replaceable item: SMR source code is: PA, PB, PC, PG or PH
    Asset itself or a subcomponent associated with a measurement location
    Other criteria?
      Repairable and reusable items that can be installed/reinstalled on one or multiple platforms of different models: SMR recoverability code is neither A nor Z
      Serialized – has a unique identifier: SN/VIN/?
      Others(?)
  Other serialized items:
    Sensors
    Others(?)
Asset Instance Component Tree – cloned from its model prototype tree
Site – Each asset has a site for its instance components

## Slide 17: Hypothetical Assets
M1
M1:A1
M1:R2
M1:R1
M2
M2:R3
M3
M1:R1R3
M1:R1P1
M1:R2R3
M1:R2P1
A1
A1:A1
A1:R2
A1:R1
A2
A2:R3
A2:P1
A3
A1:R1R3
A1:R1P1
A1:R2R3
Assets
Models
A4
A4:R3
A4:P1
A5
A1:R2P1
Inheritance (clone) relationship
A3:A1
A3:F1
A5:A1
A5:F1
A4:A2
A4:F2
A4:F1
A2:A2
A2:F2
A2:F1
A1:A3
A1:R2F1
A1:R1F1
A1:R2F2
A1:R1F2
M1:A3
M1:R2F1
M1:R1F1
M1:R2F2
M1:R1F2
M2:A2
M3:A1
M2:F2
M3:F1
M2:F1
M2:P1
Note: 1.Alarm entries are not cloned for instance measurement locations.
2. Each asset has an instance (as-built) segment tree.
Site A1
Site M1
Site A2
Site M2
Site M3
Site A3
Site A4
Site A5
M1:R3
A1:R3

## Slide 18: Assets in Registry
Each asset has an instance site in site table
  If an asset doesn’t have a NIIN, but has CAGE/PartNo, search site table for a surrogate NIIN; if not found, a unique surrogate NIIN will be assigned to the model (start at 1000000000 and increase by 1)
  Site code = MACOM asset site + 1 for the first asset site; increase by 1 for next added asset site
  Site id = NIIN
  Site type = asset type of NIIN in asset_type table
  User tag identification = Asset ID (SN/VIN/?), NIIN (real or surrogate)
Each asset has an entry in asset table
  Asset site = MACOM asset site
  Asset Id = 0 for the first asset; maxID+1 for next added assets
  Asset type = asset type of NIIN in asset_type table
  User tag identification = NIIN (real or surrogate) and asset ID (SN/VIN/?)
Each asset may be associated with an entry in asset_chr_data table to store other keys and additional info (e.g. CAGE/PartNo, Bumper Number, etc.)

## Slide 19: Asset Component Tree in Registry
Each asset that has a model entry in the registry has an instance component tree represented by the following MIMOSA tables:
  segment table, each component has:
    Segment site = Asset instance site
    Segment Id = Same Id as the prototype segment from which it was cloned
    Segment type = Same type as the prototype segment from which it was cloned
    User Tag Identification = Top segment: Asset ID, NIIN (real or surrogate) ; subsegments: same type as the prototype segment from which it was cloned
    Each segment may be associated with an entry in segment_chr_data table to store other keys and additional info (e.g. CAGE/PartNo)
  sg_network_connect table: each parent-child component relationship has an entry using the ‘Component Structure Network’
  segment_child table: each inheritance (clone) relationship has an entry

## Slide 20: Asset Registration Process
Add/update an asset
Synchronize the instance segment tree and measurement configuration of an asset with its prototype segment tree and measurement configuration
Input:
Mandatory:
  NIIN or CAGE/PartNo
  Asset ID: SN/VIN/Other IDs
  MACOM
Conditional: Name (for new asset)
Optional: other info
Output:
A site for the asset exists in the site table
A asset type for the asset exists in the asset_type table
New or updated asset exist in the asset table
New or updated instance segments exist in the segment table for an asset that has a model in the registry
Entries in the se_network_connect table exist to define the component relationships in the instance segments
Entries in the segment_child table exist to define component inheritance relationships in the instance segments
Asset Registration Process

## Slide 21: Replaceable Unit Installation Criteria
Reusable Asset – Identified by NIIN and asset ID: SN/VIN/Other IDs(?):
  Installed to a target component of the same model in a parent asset
  An installed RU is associated with one or more components in its ascendant asset(s)

## Slide 22: Hypothetical RU Installation
M1
M1:A1
M1:R2
M1:R1
M2
M2:R3
M3
M1:R1R3
M1:R1P1
M1:R2R3
M1:R2P1
Installation relationship
A1
A1:A1
A1:R2
A1:R1
A2
A2:R3
A2:P1
A3
A1:R1R3
A1:R1P1
A1:R2R3
Assets
Models
A4
A4:R3
A4:P1
A5
A1:R2P1
Inheritance relationship
A3:A1
A3:F1
A5:A1
A5:F1
A4:A2
A4:F2
A4:F1
A2:A2
A2:F2
A2:F1
A1:A3
A1:R2F1
A1:R1F1
A1:R2F2
A1:R1F2
M1:A3
M1:R2F1
M1:R1F1
M1:R2F2
M1:R1F2
M2:A2
M3:A1
M2:F2
M3:F1
M2:F1
M2:P1
Note: A n RU is also installed on all ascendant assets, e.g. A3 is installed on both A2 and A1 because A2 is installed on A1. All installation relationships are stored for easy look up.
Site A1
Site M1
Site A2
Site M2
Site M3
Site A3
Site A4
Site A5
A1:R3
M1:R3

## Slide 23: Replaceable Unit Installation in Registry
An installed RU asset is associated with one or more entries in asset_on_segment table, each of which defines an installation relationship from the asset to an instance segment of an ascendant asset

## Slide 24: Replaceable Unit Installation Process
Install or replace an RU on a target segment of a parent asset
Associate all sub-RUs to corresponding subsegments of the parent asset segment tree
Associate all corresponding subsegments in the instance segment trees of all ascendant assets to the RU
Input:
Mandatory RU ID:
  NIIN or CAGE/PartNo
  Asset ID: SN/VIN/Other IDs
Mandatory: Target segment of the parent assent
Output:
An entry in the asset_on_segment table exists to define the installation relationship between the RU and the target segment
Entries in the asset_on_segment table exist to define the installation relationships between the RU and its corresponding sub-segment in the parent asset segment tree
Entries in the asset_on_segment table exist to define the installation relationships between a sub-RU of the RU and a corresponding subsegment in an instance segment tree of a ascendant asset.
Replaceable Unit Installation Process

## Slide 25: Furture Work and Considerations
Work with TACOM and LOGSA to create common registration processes for all MACOMs
Use some platforms and measurement configurations for CECOM EOA II to manually populate data to a registry and validate the processes
Create a reusable tool (with XML as input) to automate the processes
Use the tool to populate all platforms and measurement configurations for CECOM EOA II to a CLOE SV-11 compliant database
Handle associations between measurement locations
Create process to delete registered objects
Create process to update IDs/Keys (e.g. replace a surrogate NIIN with a real NIIN)

## Slide 26: Backup Slides

## Slide 27: Model Registration Process
Add a new model and its associated prototype component tree for a class of platforms or RUs as well as synchronize its previously added assets with the model
Add new prototype components for an existing model and synchronize the cloned instance component trees for existing assets of the model as well as the cloned prototype component trees of ascendant models with the component trees of the updated model
Input:
Mandatory: Model
  Mandatory: NIIN or CAGE/PartNo
  Conditional: Name (for new model)
  Conditional: SMR Code (for RU)
Mandatory :Type
  Platform: ‘Ground Platform‘ or ‘Tactical Wheel Vehicle System‘
  RU: ‘SRU’
Optional: Other info (e.g. manufacturer)
Optional: Component tree, each component in the tree has:
  Mandatory: Name,
  Optional:
  SMR code,
  NIIN or CAGE/PartNo
Output:
A site for the model prototype segments exists in the site table
A asset type for the model exists in the asset_type table
New or updated model entries exist in the model table for the model and the models of valuable sub-RUs
New or updated prototype segments exist in the segment table for the model and the models of valuable sub-RUs
Entries in the se_network_connect table exist to define the component relationships in the prototype segments
Entries in the segment_child table exist to define component inheritance relationships in the prototype segments
The cloned prototype segment subtrees in all existing ascendant models are in sync with the model
The cloned instance segment tree for all existing assets of the model are in sync with the model
The assets of a new model previously added are in sync with the model
Model Registration Process

## Slide 28: Model Registration Process

## Slide 29: Prototype Segment Creation Subprocess
Create new descendent prototype segments for the new subcomponents in a model subcomponent tree and add them to a prototype segment tree
Input:
Mandatory: Top segment of a prototype tree
Mandatory :Model subcomponent tree , each component has:
  Mandatory: Name,
  Conditional:
  SMR code,
  NIIN or CAGE/PartNo
Output:
New descendent prototype segments were added to segment table for all new components in the model subcomponent tree
Existing descendent prototype segments were updated accordingly
Entries in se_network_connect table exist to define the component relationships in the prototype tree
Entries in segment_child table exist to define component inheritance relationships in the prototype tree
Prototype Segment Creation Process

## Slide 30: Prototype Segment Creation Subprocess

## Slide 31: Segment Tree Synchronization Subprocess
Synchronize a cloned segment tree (either instance or prototype) with a given prototype segment tree
Input:
Mandatory: Top segment of the prototype segment tree
Mandatory: Top segment of a cloned segment tree to be synchronized with the prototype tree
Mandatory: Cloned site is a prototype or instance site
Output:
The cloned segment tree matches the given prototype segment tree
Segment Tree Synchronization Subprocess

## Slide 32: Segment Tree Synchronization Subprocess

## Slide 33: Prototype Measurement Configuration Process
Add/update prototype measurement locations of a model
Synchronize the instance measurement locations for all existing assets of the model with the updated prototype measurement locations
Synchronize the cloned measurement configuration for all ascendant models with the measurement configuration of the model
Input:
Mandatory: Model NIIN
Mandatory: List of measurement locations, each of the locations includes:
  Mandatory: name, type(Data event group, DA, DM, SD, HA, PA, AG)
  Mandatory: segment or asset indicator, monitored segment
  Conditional: engineering unit (for CBM layers), update interval (for DA)
  Conditional (for CBM layers): alarm info (e.g. alarm type, min, max, typical, effective data, etc.)
  Optional: data source type
Output:
New or updated prototype measurement locations exist in the meas_location table for the model
New or updated alarm entries exist for each measurement locations of CBM layer in the num_alarm_reg table
The cloned measurement locations for all existing ascendant models are in sync with the measurement locations of the model
The instance measurement locations for all existing assets of the model are in sync with the measurement locations of the model
Prototype Measurement Configuration Process

## Slide 34: Prototype Measurement Configuration Process

## Slide 35: Measurement Location Synchronization Subprocess
Synchronize the measurement locations on an instance or a prototype segment tree with the measurement locations on a prototype segment tree
Input:
Mandatory: Top segment of the prototype segment tree
Mandatory: Top segment of a cloned segment tree on which the measurement locations to be synchronized with the measurement locations on the prototype tree
Option: ‘for instance’ , ‘for prototype’
Conditional: asset (for instance)
Output:
The measurement locations on the cloned segment tree matches the measurement locations on the prototype segment tree
If the option is ‘for prototype’: the alarm entries for the measurement locations on the cloned segment tree matches the alarm entries for the measurement locations on the prototype segment tree
Measurement Location Synchronization Subprocess

## Slide 36: Measurement Location Synchronization Subprocess

## Slide 37: Asset Registration Process
Add/update an asset
Synchronize the instance segment tree and measurement configuration of an asset with its prototype segment tree and measurement configuration
Input:
Mandatory:
  NIIN or CAGE/PartNo
  Asset ID: SN/VIN/Other IDs
  MACOM
Conditional: Name (for new asset)
Optional: other info
Output:
A site for the asset exists in the site table
A asset type for the asset exists in the asset_type table
New or updated asset exist in the asset table
New or updated instance segments exist in the segment table for an asset that has a model in the registry
Entries in the se_network_connect table exist to define the component relationships in the instance segments
Entries in the segment_child table exist to define component inheritance relationships in the instance segments
Asset Registration Process

## Slide 38: Asset Registration Process

## Slide 39: Replaceable Unit Installation Process
Install or replace an RU on a target segment of a parent asset
Associate all sub-RUs to corresponding subsegments of the parent asset segment tree
Associate all corresponding subsegments in the instance segment trees of all ascendant assets to the RU
Input:
Mandatory RU ID:
  NIIN or CAGE/PartNo
  Asset ID: SN/VIN/Other IDs
Mandatory: Target segment of the parent assent
Output:
An entry in the asset_on_segment table exists to define the installation relationship between the RU and the target segment
Entries in the asset_on_segment table exist to define the installation relationships between the RU and its corresponding sub-segment in the parent asset segment tree
Entries in the asset_on_segment table exist to define the installation relationships between a sub-RU of the RU and a corresponding subsegment in an instance segment tree of a ascendant asset.
Replaceable Unit Installation Process

## Slide 40: Replaceable Unit Installation Process

## Slide 41: Asset On Segment Subprocess
If an RU asset is provided, associate the RU asset with the target segment
Associate all sub-Rus installed on subsegments of a source segment, if any, to corresponding subsegments of a target segment.
Input:
Source segment
Target segment
RU asset to be installed on the target segment(optional)
Output:
If an RU asset is provided, an entry exists in the asset_on_segment table to define the installation relationship between the RU asset and the target segment
Entries exist in the asset_on_segment table to define the installation relationships between a sub-RU assets of the source segment and its corresponding sub-segment of the target segment
Asset On Segment Subprocess

## Slide 42: Asset On Segment Subprocess